## Slide 1: Development of an Intermittent Computing Architecture for Machine Learning on configurable platforms
Michele Fragasso

## Slide 2: Outline
DNNs
Handwritten Number Classification
VHDL Implementation
Integrating with NORM

## Slide 3: Neuron
Every Neuron has its own weights and biases.
The parameters results from a training algorithm.
Every Neuron outputs only one value.

## Slide 4: Fully Connected Neural Network
Every Layer can be seen as an entities with a number of inputs equal to the number of neuron of the previous layer and a number of outputs equal to its number of neurons.
1
2
3
4
5
1
2
3
1
2
3
4
1
2
3
4
1
2
3
4

## Slide 5: Handwritten numbers detenction
Mnist DataSet
Greyscale Images;
28x28 pixel;
784 values

## Slide 6: Overall DNN - Fully Connected Neural Netowork
INPUT LAYER: Every neuron of the first layer is connected to every pixel of the image.
OUTPUT LAYER: 10 neurons. Every neurons’ output value reflects the level of confidence the DNN assign that specific number to the input image.
Mnist Package is used to train the DNN; a python script is used to train it; the number of layers of neurons can be modified;

## Slide 7: Possible Implementations
Parallel implementation
The whole weighted sum is computed;
CONS
There is the need of a number of data lines equal to the numbers of the input of the layer;
There may be overcrowding of data lines for a given layer;
If the system shuts down in the middle of the computation the weighted sum must be computed from scratch;
Serial/Sequential implementation
At every clock cycle only one term is computed;
PROS
The computational power is spread over the number of total clock cycles required to compute the weighted sum;
The architecture has only one data line for the input;
It enables saving of parts cumulative sum;
SEQUENTIAL IMPLEMENTATION HAS BEEN IMPLEMENTED
weighted product

## Slide 8: Neuron Implementation
The weights and bias indentifying the neurons are stored into non-volatile ROMs which are accessed in a sequential fashion;
An accumulator is used for storing the cumulative weighted sum;
Control Logic is implemented by using a Finite State Machine
weighted product

## Slide 9: Finite State Machine
FINITE STATE MACHINE
IDLE;
W_SUM;
B_SUM;
ACT_FUN;
FINISHED;
The FSM has been moved outside and modified slightly.

## Slide 10: Layer Implementation
1
2
3
4
5
1
2
3
1
2
3
4
1
2
3
4
1
2
3
4
THIRD LAYER OUTPUTS
FOURTH LAYER OUTPUTS

## Slide 11: Layer Implementation

## Slide 12: Finite State Machine

## Slide 13: TestBench Layer
Input Array
Layer: 30 inputs/30 outputs
Triggering the Layer and Starting computation
Adding Bias, Apply activation Logic
addr_TC is set to 1, stop the weighted sum computation
Updating register, Holding the output values of the layers. Accessing the neurons’ output
All the neurons’ output registers are updated, data is now ready to be fetched
We access neuron 7

## Slide 14: DNN Implementation
Layer output is fetched through this line

## Slide 15: TestBench DNN

## Slide 16: Testbench DNN

## Slide 17: Testbench DNN

## Slide 18: Testbench DNN

## Slide 19: Testbench DNN

## Slide 20: Integrating with NORM - Saving The DNN state
NORM Framework Overview
Coupling with NORM

## Slide 21: The intermittency emulator
Based on a voltage trace, this module pulls down a reset pin to erase the content of any volatile registers;

## Slide 22: NV Register Architecture
The non-volatile register is implemented by using an block-ram within the FPGA.
Data is saved by storing all the content of Volatile Architecture RAM to the non-volatile register.
Data is retrieved by loading the content of the NV_REG and loadin g it inside the RAM.

## Slide 23: NV_REG FSM
This FSM plans when to carry normal, backup or recovery operations.
The actual implementation resides within the volatile architecture

## Slide 24: VOLATILE ARCHITECTURE
TO THE NV_REG
TO THE FSM_NV_REG
FROM FSM_NV_REG
FROM THE NV_REG
INTERMITTENCY EMULATOR

## Slide 25: VOLATILE ARCHITECTURE FSM
Surpivises the recovery, backup and normal operation of the volatile architecure. It follows the imperative commands coming from the Non-Volatile FSM.

## Slide 26: OVERALL ARCHITECTURE
POWER_RESET
NV_REG
FSM_NV_REG

## Slide 27: Coupling the DNN with NORM
NV_REG
FSM_NV_REG
NV_REG
NV_REG
TASK_STATUS
TASK_STATUS
TASK_STATUS
POWER_RESET
TASK_STATUS

## Slide 28: Coupling the layer with NORM
NV_REG
FSM_NV_REG
POWER_RESET
The internal FSM of the layer is now also required to interact with the non-volatile FSM machine and carry the operation demanded by FSM_NV_REG.
The FSM will be augumented to implement recovery and backup operation from and and to the NV_REG.
FSM will also need to be extended to support backup, recovery, and do operation

## Slide 29: What data to save ?
State of currently active layer.
State of previous layer
NEURON
LAYER

## Slide 30: Neuron Added Pins
POWER_RESET
DATA_OUT_SAVE
DATA_OUT_REC
CUM_SUM_SAVE
CUM_SUM_REC

## Slide 31: Layer Added Pins
FSM_STATE_SAVE
FSM_STATE_REC
ADDR_GEN_REC
ADDR_GEN_SAVE

## Slide 32: NV_REG CONTENT
NOTHING
OUTPUT
W_SUM
0 | 1
1 | D.C.
2 | D.C.
32 | D.C.
0 | 2
1 | 
2 | 
30 | 
31 | D.C.
32 | D.C.
0 | 2
1 | 
2 | 
30 | 
31 | D.C.
32 | D.C.
0 | 
1 | 
2 | 
30 | 
31 | 
32 | 
0 | 
1 | 
2 | 
30 | 
31 | 
32 | 

## Slide 33: DNN Overall Architecture
NV_REG
FSM_NV_REG
NV_REG
NV_REG
TASK_STATUS
TASK_STATUS
TASK_STATUS
OUT_V_SET
OUT_V_SET
OUT_V_SET